## Slide 1: CalLite Delivery Shortage
Z.Q. Richard Chen
DWR

## Slide 2: List of Changes to CL_SharingFix_092812
Copy the following wresl files from CalSim:
  Shortage.wresl with minor modification
  Shortage_cvp_n.wresl with minor modification
  Shortage_cvp_s.wresl with minor modification
  Shortage_swp.wresl with minor modification
  Shortage_prf_n.wresl with minor modification
  Scwa.wresl with minor modification
Create a new wresl files based on CalSim:
  Shortage_CalLiteExtra
Copy the following table from CalSim:
  Refuge.table

## Slide 3: List of Changes to CL_SharingFix_092812
Modefined following wresl files:
  Weigth-table, add three weights
    [D168C_EXCESS_PMI,-200],
    [D168C_FRWP_PMI,5000],
    [D168C_OTHER_PMI,4900],
  Swp_bound_del
    see next slide for details
  Main_BO_AllFixes090412
Part B: | Part C: | UNITS
D300_PMI | FLOW-DELIVERY | CFS
DEM_C136B_PRF | DEMAND-RF | TAF
DEM_D168C_FRWP_PMI | DEMAND-CVP-MI | TAF
DEM_D168C_OTHER_PMI | DEMAND-CVP-MI | TAF
DEM_D300_PMI_ANN | DEMAND-CVP-MI | TAF
DEM_D300_WR_ANN | DEMAND-NP-MI | TAF
DEM_SCWA_TOTAL_PMI | DEMAND-CVP-MI | TAF
Copy the following CalSim time series to the CalLite SV file:

## Slide 4: Corrections to CalSim II Codes
Swp_bound_del.wresl
  define target_d206b_pwr {value min(ad_d206b_pwr, demand_prj_69*con_d206b_pwr/con_69_total)}
  goal limit_d206b_pwr {d206b_pwr < ad_d206b_pwr}
  goal limit_d206b_pwr {d206b_pwr < target_d206b_pwr}
  define target_d206c_pwr {value min(ad_d206c_pwr, demand_prj_69*con_d206c_pwr/con_69_total)}
  goal limit_d206c_pwr {d206c_pwr < ad_d206c_pwr}
  goal limit_d206c_pwr {d206c_pwr < target_d206c_pwr}
demands_CB.wresl
  define target_D171_pag {value min(perdel_cvpag_sys*con_D171_pag , target_D17101 *(1.0+ConvLs_17101))}
  define target_D171_pag {value min(perdel_cvpag_sys*con_D171_pag , target_D17101 /(1.0-ConvLs_17101))}
  define target_D172_pag {value min(perdel_cvpag_sys*con_D172_pag , target_D17201 /(1.0-ConvLs_17201))}
  define target_D174_pag {value min(perdel_cvpag_sys*con_D174_pag , target_D17401 /(1.0-ConvLs_17401))}
  define target_D178_pag {value min(perdel_cvpag_sys*con_D178_pag , target_D17801 /(1.0-ConvLs_17801))}
  define target_D122A {value min(perdel_cvpsc_sys * con_14301SC , target_D14301SC /(1.0-ConvLs_14301))}
  define target_D122B {value min(perdel_cvpsc_sys * con_14501SC , target_D14501SC / (1.0 - ConvLs_14501))}
  define target_D129A {value min(perdel_cvpsc_sys * con_18301SC , target_D18301SC /(1.0-ConvLs_18301))}
  define target_D128 {value min(perdel_cvpsc_sys * con_131SC , target_D131SC /(1.0-ConvLs_131))}
Delivery Shortage = DeliveryTarget – ActualDelivery
Notes: define ad_d6_pwr {value dem_d6_pwr*taf_cfs}{value dem_d6_pwr*taf_cfs}
ad_ => Allocated Diversion Limits based on contract cuts

## Slide 5: Determine DeliveryTarget to WBAs demands_CB.wresl
goal splitD172 { D172 = D172_pag }
goal setL17201 { L17201 = D172 * ConvLs_17201} !set conveyance loss
goal limitD17201 {D17201 = target_D17201}
goal limitD172 {D172_pag < perdel_cvpag_sys*con_D172_pag }
goal limitD172_1 {D172_pag < target_D17201 + L17201}
target_D172_pag = min(perdel_cvpag_sys*con_D172_pag ,
target_D17201 /(1.0-ConvLs_17201))
Notes: demands_CB.wresl
When NODOS does not exist, D_171_NDS = 0

## Slide 6: CalLite Delivery Shortage Comparison
 |  | SHORT_SWP_TOT_N | SHORT_CVP_TOT_N | SHORT_SWP_TOT_S | SHORT_CVP_TOT_S
BDCPupdates | MAX_Annual | 232.6 | 224.3 | 825.7 | 71.6
 | Critical | 18.4 | 137.4 | 38.7 | 5.6
 | Dry | 0.7 | 64.0 | 114.9 | 3.3
 | BNormal | 4.5 | 56.8 | 91.8 | 0.0
 | ANormal | 0.4 | 57.9 | 129.9 | 0.2
 | Wet | 7.4 | 60.2 | 107.0 | 5.4
 | WY1928_34 | 0.5 | 158.3 | 10.2 | 0.0
 | WY1986_92 | 0.7 | 104.4 | 110.0 | 0.0
 | WY1922_03 | 6.4 | 76.8 | 106.8 | 3.5
 |  | SHORT_SWP_TOT_N | SHORT_CVP_TOT_N | SHORT_SWP_TOT_S | SHORT_CVP_TOT_S
CL_SharingFix | MAX_Annual | 232.6 | 223.7 | 1052.6 | 160.4
 | Critical | 18.3 | 134.6 | 117.7 | 12.4
 | Dry | 0.7 | 63.7 | 101.0 | 6.8
 | BNormal | 4.5 | 55.9 | 130.1 | 0.0
 | ANormal | 0.4 | 56.7 | 211.6 | 1.4
 | Wet | 7.4 | 60.1 | 121.0 | 6.7
 | WY1928_34 | 0.4 | 157.5 | 177.3 | 0.0
 | WY1986_92 | 0.6 | 100.0 | 59.5 | 0.0
 | WY1922_03 | 6.4 | 75.9 | 140.5 | 6.1

## Slide 7: System Flow Comparison
DWRFix: DWR code fix and BOR code fix refinement, BDCP updates, Base: Released Version on 10/2011. Assumptions: Future LOD and Demand, D1641+BO |  |  |  |  |  |  |  |  |  |  |  | 
 | 1922-2003 |  |  |  | 1929-1934 |  |  |  | 1987-1992 |  |  | 
 | BDCP_updates | CL_SharingFix | Diff | % Diff | BDCP_updates | CL_SharingFix | Diff | % Diff | BDCP_updates | CL_SharingFix | Diff | % Diff
River Flows |  |  |  |  |  |  |  |  |  |  |  | 
Trinity R blw Lewiston | 697.5 | 700.7 | -3.2 | -0.5% | 411.5 | 411.5 | 0.0 | 0.0% | 472.0 | 472.0 | 0.0 | 0.0%
Trinity Export | 532.7 | 528.7 | 4.0 | 0.8% | 402.1 | 378.2 | 23.9 | 6.3% | 480.3 | 449.5 | 30.8 | 6.8%
Clear Cr blw Whiskeytown | 129.4 | 129.3 | 0.1 | 0.1% | 100.6 | 100.6 | 0.0 | 0.0% | 116.2 | 116.2 | 0.0 | 0.0%
Sacramento R @ Keswick | 6248.8 | 6244.0 | 4.9 | 0.1% | 4065.1 | 4017.7 | 47.4 | 1.2% | 4599.6 | 4504.6 | 95.0 | 2.1%
Sacramento R @ Red Bluff | 8247.5 | 8236.0 | 11.5 | 0.1% | 5137.3 | 5083.4 | 53.9 | 1.1% | 5751.9 | 5648.1 | 103.9 | 1.8%
Sacramento R @ Wilkins Slough | 6629.6 | 6618.0 | 11.6 | 0.2% | 4068.1 | 4014.2 | 53.9 | 1.3% | 4881.5 | 4777.6 | 103.9 | 2.2%
Oroville Dam Release | 3926.6 | 3928.6 | -2.0 | 0.0% | 2225.8 | 2222.5 | 3.2 | 0.1% | 2113.8 | 2090.4 | 23.4 | 1.1%
Feather R blw Thermalito | 3175.7 | 3178.1 | -2.4 | -0.1% | 1556.6 | 1555.1 | 1.5 | 0.1% | 1472.1 | 1451.7 | 20.4 | 1.4%
YubaFeather Confluence | 1453.8 | 1453.8 | 0.0 | 0.0% | 589.9 | 589.9 | 0.0 | 0.0% | 578.0 | 578.0 | 0.0 | 0.0%
Feather R @ Confluence | 5608.9 | 5611.8 | -2.9 | -0.1% | 2215.8 | 2214.5 | 1.3 | 0.1% | 2545.5 | 2525.8 | 19.7 | 0.8%
Sacramento R @ Verona | 13230.0 | 13234.9 | -4.8 | 0.0% | 6857.1 | 6801.8 | 55.2 | 0.8% | 8077.7 | 7954.2 | 123.6 | 1.6%
American R blw Nimbus | 2388.1 | 2386.0 | 2.2 | 0.1% | 1263.9 | 1233.2 | 30.7 | 2.5% | 1123.5 | 1091.3 | 32.2 | 3.0%
Delta Inflow | 21601 | 21590 | 11.0 | 0.1% | 9897 | 9811 | 86.1 | 0.9% | 10482 | 10325 | 156.7 | 1.5%
Sacramento R @ Hood | 15663.9 | 15667.0 | -3.1 | 0.0% | 8245.6 | 8159.5 | 86.1 | 1.1% | 9114.7 | 8958.1 | 156.6 | 1.7%
Yolo Bypass | 2247.1 | 2233.0 | 14.1 | 0.6% | 99.9 | 99.9 | 0.0 | 0.0% | 141.3 | 141.3 | 0.0 | 0.0%
Mokelumne R | 666.1 | 666.1 | 0.0 | 0.0% | 205.6 | 205.6 | 0.0 | 0.0% | 155.0 | 155.0 | 0.0 | 0.0%
San Joaquin R d/s Calaveras | 3024.3 | 3024.3 | 0.0 | 0.0% | 1346.4 | 1346.4 | 0.0 | 0.0% | 1070.7 | 1070.7 | 0.0 | 0.0%
Delta Outflow | 15782 | 15770 | 12.0 | 0.1% | 5621 | 5660 | -38.7 | -0.7% | 6169 | 6183 | -14.5 | -0.2%
Required | 5069 | 5067 | 2.3 | 0.0% | 4146 | 4141 | 5.2 | 0.1% | 4045 | 4043 | 2.0 | 0.0%
Delta Exports | 4853 | 4857 | -3.1 | -0.1% | 3096 | 2964 | 131.6 | 4.4% | 3048 | 2883 | 165.1 | 5.7%
Banks SWP | 2608.5 | 2588.3 | 20.3 | 0.8% | 1675.2 | 1468.8 | 206.4 | 14.0% | 1495.5 | 1298.5 | 197.0 | 15.2%
Banks CVP | 63.6 | 59.3 | 4.3 | 7.3% | 9.2 | 20.8 | -11.6 | -55.6% | 28.7 | 30.7 | -2.1 | -6.8%
Tracy | 2181.3 | 2209.0 | -27.7 | -1.3% | 1420.7 | 1495.4 | -74.7 | -5.0% | 1552.9 | 1584.8 | -31.9 | -2.0%
SWP Deliveries | 2587 | 2564 | 23.0 | 0.9% | 1578 | 1427 | 151.1 | 10.6% | 1414 | 1265 | 148.7 | 11.8%
Table A | 2468.0 | 2430.0 | 38.0 | 1.6% | 1521.1 | 1369.9 | 151.3 | 11.0% | 1393.3 | 1224.6 | 168.7 | 13.8%
Article 21 | 49.0 | 56.0 | -7.0 | -12.5% | 49.7 | 37.6 | 12.1 | 32.2% | 16.9 | 14.1 | 2.8 | 20.0%
Article 56 | 70.0 | 78.0 | -8.0 | -10.3% | 7.3 | 19.6 | -12.3 | -62.7% | 3.4 | 26.3 | -22.8 | -86.9%
CVP SOD Deliveries | 2358 | 2381 | -22.9 | -1.0% | 1418 | 1462 | -44.3 | -3.0% | 1628 | 1658 | -30.4 | -1.8%